# CS241 Project 3
## Synopsis
Implement the Triangle Scanline algorithm with Z-buffer depth testing.
## Instructions
Use the previous project (the clipper) as a starting point for this project. At each call to DrawScene (in render.cpp)
- ensure you have a Z-buffer of the size specified by DrawScene's width and height parameters.
- Extract all the polygons from the scene,
- transform vertices (from Project 1),
- clip to the view frustum (Project 2),
- transform to pixel coordinates,
  (x,y,z,w) ~toward~ (x/w `*` width/2 `+` width/2, ~ y/w `*` height/2 `+` height/2, ~z/w) ,
- split polygon into triangles, and
- render each triangle to the screen via the Z-buffer/scanline algorithm.
Several modifications will need to be made to the current framework to put OpenGL into a pixel drawing mode rather than a polygon drawing mode. (See the provided example render.cpp for details.)
  - Use glDisable(GL_DEPTH_TEST) to disable OpenGL's depth testing.
  - Use gluOrtho2D(0,width,0,height) to setup individual pixel addressing.
  - Use glBegin(GL_POINTS) to specify pixel drawing.
  - Use glPointSize(1.0) to specify that points will be a single pixel in size.
  - Use glMaterialfv(...) and glNormal3fv(...) to setup the lighting parameters.
  - Use glVertex2f(px, py) to draw a single pixel at pixel coordinate (px,py).
## Project Report
As always, submit a succinct project report with your project, describing anything I need in order to understand your implementation. Place your project report in a text file named report.txt (or report.doc or report.odt if you (unnecessarily) insist on producing a formatted document).
## To submit
Create a zip file containing only your report, and your source code *.cpp, *.h and *.vcproj files and nothing else. Submit the zip file via the Moodle class web page.
## Grading Basis
Grading will be on a 100 point basis, with the following distribution:
- Accuracy: 60%, judgment based on looking at the results on the screen.
- Efficiency: 20%, judgment based on frame rate.
- Code: 10%, judgment based on looking at the code for proper implementation and reasonable coding and commenting practices.
- Project report: 10%, judgment based on how succinctly and accurately the project report describes your implementation.